## Slide 1: Nutrient Removal Project: Oxygen Requirements
DO probe
Stir bar
Air
Temperature probe
Pressure sensor
History of Human Waste
Nutrient Removal Project
Dissolved oxygen measurements
Oxygen Transfer

## Slide 2: Excreta Disposal: Land Application
When population densities were low excreta disposal was an individual problem.
As cities grew it was no longer possible for individuals to practice “direct land application.”
Before 1800 city residents placed “night soil” in buckets along streets and workers emptied the waste into “honeywagon” tanks.
The waste was transported to rural areas for disposal on farm land. The honeywagon system preserved the essential feature of land application of the waste.
Nutrient Recycle

## Slide 3: Toilets
Until about 1850 even the members of Congress were required to go outside and walk down Capitol Hill to privy facilities.
1850-1900: The flush toilet came into general use in the U.S. during the last half of the nineteenth century.
Introduction of the toilet coincided with ______ _____.
central heat

## Slide 4: Night Soil vs. Sewers
Dutch engineer Charles Liernur advocated dry disposal. He claimed underground sewers would be the source of ________ _____ giving rise to sickness and death.
English engineer Baldwin Latham supported water carriage of excreta. Latham proceeded with the installation of a water carriage system for Croydon, where he was engineer of public works.
The water carriage system led to an immediate decrease in the death rate in the cities that installed it.
noxious gases
I’d like to see the data!
But what about the cities downstream?

## Slide 5: Conversion of Storm Sewers to “Sanitary” Sewers
Toilets were connected to existing storm sewers
The storm drain systems discharged directly to streams, lakes, and estuaries without treatment
Treatment of wastewater only became an issue after the self-purification capacity of the receiving waters was exceeded and ________ __________ became intolerable
nuisance conditions
Notes: What were the nuisance conditions?

## Slide 6: Wastewater into Streams: Enter Environmental Engineering!
Drinking water treatment began to receive attention in the 1800s.
London, and cities on the Great Lakes found themselves draining their raw sewage into the same body of water from which they took their drinking water.
  Chicago solved this problem by reversing the flow of the Chicago river and sending its waste through a canal to the Illinois River to the Mississippi.
  English engineers tackled the problem by developing treatment techniques for both wastewater and drinking water.

## Slide 7: Evolution of Treatment Goals
Solids (sedimentation)
BOD (activated sludge)
Nitrification (convert ammonia to nitrate)
Denitrification (convert nitrate to N2)
Phosphorus (get bacteria to take up phosphorus so phosphorus can be removed with the sludge)

## Slide 8: Nutrient Removal Project
The challenge: build an automated wastewater treatment plant that removes organic carbon from a synthetic feed
Batch or continuous feed
Maintain high cell concentrations using sedimentation
We need to monitor oxygen levels
We need air (oxygen)…

## Slide 9: NRP Context… Can you control the oxygen concentration?
Suppose that you knew the desired rate of oxygen transfer into the reactor
How would you set the air flow rate?

## Slide 10: Air Supply Design Questions
How much oxygen will be required by the wastewater?
How much air will need to be supplied?
Number of diffusers
Reactor configuration (shallow vs. deep)
How will we supply the air?
  Peristaltic pump
  Laboratory compressed air (100+ kPa source) with air flow controller
BOD
Q*BOD
Tradeoff cost and efficiency

## Slide 11: Diffuser Air Supply Design
If we use the laboratory air supply (100 kPa) for the NRP how could we regulate air flow?
We have computer controlled solenoid valves.
Electromagnet turns on and off
1. Valve Body | 4. Coil / Solenoid | 7. Plunger
2. Inlet Port | 5. Coil Windings | 8. Spring
3. Outlet Port | 6. Lead Wires | 9. Orifice
Notes: Easy solutions
Variable duty cycle
A variable control without really knowing what you are setting
Great solution
Somehow measure the flow rate and control it
Airflow rate that doesn’t vary much

## Slide 12: Nutrient Removal Project
Project Expectations
Project rationale (context)
Nitrogen Removal
Sequencing Batch Reactor Operation
Software that makes decisions
Research Ideas
4 h
BOD0
Biomass

## Slide 13: Project Expectations
3 weeks of plant operation 4 hours per week outside of class
Data collection and data analysis used for plant control (evidence of good engineering)
Maintain good records of what you did and what you learned
Collaboration between teams is encouraged
What is success? – measure oxygen uptake rate as a function of time!
Cite source!
SBR design

## Slide 14: SBR OPERATION for Activated Sludge
4 h
BOD0
Biomass
Add tap water
Add 20x concentrated waste
Aerate
Settle
Discharge Clean Supernatant

## Slide 15: Plant Flow Rate
HRT of approximately 6 hours
MLVSS (mixed liquor volatile suspended solids)
  3000 mg/L using clarifier
4 L tank therefore ___ L/day (per plant)
16
16 L/d * 6 weeks * 7 d/week * 8 plants = 5400 L

## Slide 16: Suspended Solids Targets and Measurements
Key to reactor success is keeping adequate MLVSS in the reactor
Solids retention time is approximately 10 days
Target MLVSS of approximately 3 g/L
If reactor volume is 4 L then waste ___ g/day
Effluent concentration of solids needs to be very low
1.2

## Slide 17: SBR Feed and Waste Volumes
What is the recycle volume?
What is the volume of waste (tap+concentrate)
  What is the volume of tap water?
  What is the volume of concentrated waste?
4 h
X = 3 g/L
6 hr
4 L
1 hr
Xr=10 g/L
1.2 L
2.8 L
140 mL
2.66 L
12 g

## Slide 18: SBR States and Exit Decision Variables
State Exit decision variable
___________ ____________
___________ ____________
___________ ____________
___________ ____________
___________ ____________
Drain
Settle
Fill with waste
Fill with water
Time or O2 consumption
Tank depth or Time
Time (peristaltic pump)
Tank depth
Aerate
Time
4 h

## Slide 19: Synthetic Feed Composition
Organic carbon
Nitrogen
Phosphate and pH

## Slide 20: Feed Characteristics
Completely soluble at feed concentration
325 mg/L COD (Chemical Oxygen Demand)
40.9 mg/L nitrogen

## Slide 21: Organic Feed Lines
What will happen if the organic feed line holds a high concentration of organics at room temperature for several weeks?
Why might this be a problem? _____________________
How can you solve this problem? _____________________________
Clog the tubes and the valves
Purge organic feed line with tap water
Not necessary for 1 week of operation

## Slide 22: Dissolved Oxygen Control
Suppose the fill cycle just ended
How could you set the initial aeration rate?
How could you correct the aeration rate?
What are some potential control strategies?
  _____________________
  _______________________
  ________________________________
Aerate at constant rate
On/Off aeration based on DO level
Variable aeration based on DO level
On-off controller is available as an external function

## Slide 23: Project Constraints
1 peristaltic pump
6-24 V devices (Valves, stirrer)
1-110 V device can be turned on and off using a 24 V control
  The 110 V device can be controlled by a 24 V control that also controls a valve
1 pH sensor, 1 DO sensor, 4 pressure sensors

## Slide 24: This Week’s Objectives
Build a sequencing batch reactor that includes:
Aeration
  Cycled valve in air line using accumulator
Stirring
Automated Empty/Fill-Dilute cycle
Configured sensors, set points, rules, and states

## Slide 25: This Week’s Objectives (continued)
Add the DO probe
Run Plant in automatic mode
Run your plant with fake synthetic waste!
Manually add sodium sulfite to mimic oxygen demand and see how your plant responds to low oxygen levels
Eliminate all leaks!
Ready for waste Wednesday after break

## Slide 26: Duty Cycle Function
time
\\enviro\enviro\Software\Process Controller methods\math functions\duty cycle.vi
on time
off time
on value
How could you set up the process controller to measure oxygen uptake rate using this code?
Note that the “on value” could also be calculated!

## Slide 27: Startup Checklist
Verify that all sensors are working
Replace DO membrane
Calibrate dissolved oxygen probe in saturated water
Fill reactor with mixed liquor from IWWTP activated sludge tank
Fill organic waste bottle with organic waste
Measure MLVSS (mixed liquor volatile suspended solids)
Begin in settle phase (make sure time is long enough)

## Slide 28: Standard Operating Procedure (SOP)
What is in the data files?
  All sensors
  All variables
What is in the state log files?
  Times, states, rule that caused state to change
How often must you add organic waste in the refrigerator?
Scrape sides of reactor to keep solids in suspension
Verify that fill and drain times are reasonable (no clogged valves)
Replace DO membrane (weekly)

## Slide 29: PROCESS CONTROL SOFTWARE
Data Acquisition
Process Control
  Make decisions based on data
  Send command to ProCoDA hardware to Control valves, pumps, stirrers
Data logging to file (and variable set points)
Plot data on graph
Handle Operator Commands
With averaging!

## Slide 30: Organize your Tasks
Goal is sequencing batch reactor with controlled aeration
What tasks must you accomplish?
How can you maximize your productivity?

## Slide 31: Proportional Integral Derivative Control
Kc is controller gain (tuning parameter)
TI is the integral time (tuning parameter)
TD is the derivative time (tuning parameter)
De/Dt is the error rate of change (Note that this is the same as the dissolved oxygen concentration rate of change)
is the area under the curve of the error as a function of time.
u(t) is the airflow rate that the controller sets
The Error (e) is the difference between the Process Variable and the desired Setpoint. The controller uses the proportional gain, Kc, the integral time constant, Ti, and the derivative time constant, Td, to determine an Output which drives the Error to zero.
P
I
D

## Slide 32: Proportional
Target DO
t
DO
e

## Slide 33: Proportional Integral
Target DO
t
DO
If TI is too small will get oscillating behavior

## Slide 34: Global Need for Better Nutrient Management
Coastal dead zones
Fish kills
Migratory routes blocked
Loss of diverse ocean ecosystems
Human Population
Agribusiness

## Slide 35: Long Island Sound: August 1998

## Slide 36: Long Island Sound Study
The LISS adopted a plan in 1998 to reduce nitrogen loads from human sources in the Sound by 58.5%
The greatest human sources of nitrogen in the Sound are from wastewater treatment plants discharging into waters within the Long Island Sound watershed, or directly into the Sound itself
A major component of the nitrogen reduction plan includes the need for wastewater treatment upgrades that emphasize nitrogen removal
As a result of BNR upgrades to STPs, there has been a reduction of 19.2 percent in nitrogen loading to Long Island Sound from STPs in the 1990’s (10% reduction of total)
http://www.longislandsoundstudy.net/pubs/slides/soundhealth/ch2.pdf
Notes: http://www.longislandsoundstudy.net/pubs/slides/soundhealth/ch2.pdf

## Slide 37: Gulf of Mexico
The "Dead Zone", or hypoxic zone, is a 7,000 square mile expanse of oxygen-depleted waters that cannot sustain most marine life
Human activity has resulted in a significant increase in nitrogen flux
Nitrogen sources include
  Industry
  Municipal waste water treatment
  Agriculture
    Fertilizer
    Livestock manure

## Slide 38: Bottom water hypoxia: Frequency of midsummer occurrence 1985-1999

## Slide 39: Reducing the Footprint of a Growing Global Population
reduced nitrogen
Conventional activated sludge process
  Removes BOD (organic carbon to CO2)
Nitrification
  Removes TKN (organic nitrogen and ammonia to nitrite and nitrate)
  TKN: Total Kjeldahl Nitrogen (______________)
Denitrification
  Removes nitrite and nitrate by conversion to N2 gas

## Slide 40: NITROGEN REMOVAL
Protect watersheds and coastal areas from eutrophication
Treatment of high nitrogen wastes
  Agricultural runoff
  Feedlot wastewater
  Centrate from Wastewater Treatment Plants
Treatment of drinking waters that contain elevated nitrite and nitrate

## Slide 41: Requirements for Nitrogen Removal
Electron Donor
  Organic (heterotrophs)
    Organic carbon (BOD) present in the waste
    Methanol (often added when organic carbon is already depleted)
  Inorganic (autotrophs)
    H2 or reduced sulfur (H2 can be added using bubbleless membrane dissolution)
pH
  Optimal range of 7-8
  Denitrification produces strong base

## Slide 42: Denitrification Reactions and Enzymes
Reaction Enzyme
Nitrate Reductase
Nitrite Reductase
Nitric Oxide Reductase
Nitrous Oxide Reductase
Overall process requires 5 electron equivalents per nitrogen

## Slide 43: Role of Oxygen Concentration
Inhibition of nitrogen-reductase genes
  Genes are repressed when oxygen concentration exceeds 2.5 – 5 mg O2/L
  Denitrifiers can produce reductase at relatively high O2 concentration
Inhibition of nitrogen-reductase activity
  Reaction inhibited when oxygen concentration exceeds a few tenths of a mg O2/L
  Denitrification can only occur if oxygen levels are very low somewhere in the reactor!

## Slide 44: Reactor Designs for Denitrification
Activated Sludge
Biofilm Processes
One sludge
  Biomass storage and decay
  Classical pre-denitrification
  Simultaneous nitrification with denitrification
Barnard Process
Sequencing Batch Reactor
Trick: Reserve some electron donor (organic carbon) for denitrification

## Slide 45: Tertiary Denitrification using Activated Sludge
SRT (5 d) >>HRT
High cell concentration increases reaction rate
Electron donor
No aeration!
Solids recycle
solids
hydraulic

## Slide 46: Biofilm Processes
Submerged fixed beds of rocks, sand, limestone, or plastic media
Fluidized beds of sand, activated carbon, and pellets of ion-exchange resin
Circulating beds of a range of lightweight particles
Membrane bioreactors (membrane supplies H2 and is the attachment surface)
HRT can be less than 10 minutes!

## Slide 47: Biomass Storage and Decay
Uses _______ as electron donor for denitrification
Slow kinetics of endogenous decay
BOD0
TKN0
Biomass
Sludge recycle
Sludge waste
Low BOD0
Low
Some
biomass

## Slide 48: Classical Pre-Denitrification
Uses ____ as electron donor for denitrification
Requires high mixed liquor recycle (4Qplant)
Sludge recycle
Sludge waste
BOD0
TKN0
Some BOD
Low
Some
Low BOD
Mixed liquor recycle
BOD

## Slide 49: Simultaneous Nitrification with Denitrification
Uses ____ as electron donor
Low oxygen levels permit denitrification
Can achieve 100% N removal!
BOD0
TKN0
Low BOD,
Sludge recycle
Sludge waste
BOD

## Slide 50: Barnard Process
Greater than 90% removal of TKN!
Sludge recycle
Sludge waste
BOD0
TKN0
Some BOD
Low
Some
Low BOD
3 h
11 h
1 h
3 h

## Slide 51: Barnard Sequencing Batch Reactor
Same process as Barnard carried out in a single tank
BOD0
TKN0
3 h
3 h
2 h
0.33 h
0.67 h
BOD0
TKN0
Biomass